## Slide 1: Bureau ACCESS Plans and Activities
Michael Naughton
Earth Systems Modelling Program
Bureau of Meteorology
CSIRO e-Research and
Computational and Simulation Sciences Conference
Melbourne, 3 April 2016

## Slide 2: Contents
Supercomputer upgrade project
UM International Partnership
ACCESS NWP Plans 2015-2020
ACCESS Seasonal Prediction
High resolution NWP for severe weather forecasting
  Sydney Forecast Demonstration Project
  Snowy Mountains ACCESS vs WRF comparison
  Boundary layer clouds study
  Bushfires
  TC modelling
  Darwin and North-West Shelf oil & gas domains
Maritime Continent PEG projects
Impact of improved land surface parameters: urban parameters, tree heights, topography
Soil moisture verification
Surface direct radiance fix
Transpose-AMIP examination of CABLE for NWP
HIWP clouds study

## Slide 3: National Priority Project for Petascale Supercomputer Bureau NWP and Seasonal Prediction
Funding over 7 years (2014-15 to 2020-21)
Funds used to:
  Buy a new petascale supercomputer
  Add new data storage and comms
  Host it in a commercial data centre
  Upgrade the supercomputer in 2018
  We also have to develop:
    New high resolution models
    New forecast and warning systems
Courtesy Tim Pugh

## Slide 5
International UM partnerships
Jointly developing a world leading seamless modelling system in a coordinated way
Shared science, model evaluation and technical development:
  Joint process evaluation groups
  Technical infrastructure teams
  User workshops & tutorials
Operational users complemented by:
  research partners in national / international universities & organisations
  capacity building consultancy projects with other partners
A foundation for relationships with other organisations:
  Science & model development
  Weather & climate services
  Jointly growing our businesses

## Slide 6: Advice across all timescales
Forecast lead-time
Confidence boundary
Now
Hours
Days
1-week
1-month
Seasonal
Decadal
Climate
Past climate
Analysis of past weather observations to manage climate risks
Eg. Agriculture: informs crop choice, planting to yield optimisation and minimise crop failure risk.
Predicting routine and hazardous weather conditions.
Public, emergency response, international Disaster Risk Reduction
Monthly to decadal predictions - probability of drought, cold, hurricanes….
Contingency planners, national and international humanitarian response, government and private infrastructure investment
Global and regional climate predictions.
Informs mitigation policy and adaptation choices. Impacts on water resources, heat stress, crops, infrastructure.
Notes: The Vuvuzela of seamless prediction:
The Met Office is able to make predictions on all timescales from now until a century ahead.
Analysis of past weather data is also useful to understand weather risks today – for example what is the likelihood of a particular storm event occurring.
On longer timescales the confidence boundary gets wider – however if the climate information is applied in an appropriate manner it provides extremely useful information to inform adaptation decision making.

## Slide 7
N x Global coupled model at ~10km with lead times of days to years:
Synoptic drivers
N x local coupled model at ~<=1km :
Local meteorology
PDF of local hazard:
Impacts
Met Office Modelling Strategy

## Slide 8
© Crown copyright Met Office
UK Operational Forecasting Models: Based on the Unified Model developed in partnership
Monthly to Seasonal
60 km atmosphere
¼ deg. ocean
2 ensemble members per day
Regional 4km
Global 17km
UK 1.5km
T+5 days twice/day
T+60 hour twice/day
+Regional ensemble
T+5 days twice/day
T+2 days twice/day
+Global ensemble
36 hour lead time
8 times/day
+UK ensemble 2.2 km
70 levels
85 with stratosphere
Regional models can be re-located rapidly to anywhere on the globe for weather or climate…
Notes: 8

## Slide 9
Principles of UM partnerships
The more a UM partner can invest and support itself, the more a partner can influence strategic direction of model development and own the UM
Core partners:
Commit 4FTE to joint development
Locally run and support operations & upgrades and fund central support
Member of board sets direction of joint work, controls funds & influences decisions on model development
Research partners:
Non operational users able to commit to joint development
May fund central support if needed
Associate partners:
Some commitment to joint development
Locally run and support operations & upgrades and fund central support
Feed views to the board
Board
Governing and decision body
Representative from each core partner institute
Technical advisory group
Advises board, plans and coordinates technical work
Representative from all relevant partner institutes
Science advisory group
Advises board, plans and coordinates science work
Representative from all relevant partner institutes
Ad-hoc projects
May be a need to have specific projects from time to time
Representative from all relevant partner institutes

## Slide 10
© Crown copyright Met Office
Global NWP Index (v analysis) basket % difference relative to Met Office
Maintaining our global standing

## Slide 11: Technical Infrastructure Programme Motivation
Initiated in June 2013 to resolve the priority weaknesses of the research and operational infrastructure.
Goal is a more streamlined, flexible system that is easier to use and adopt for scientific research and operational environments.
Key activities are reviewed annually in a Technical Infrastructure Programme Plan.
Program vision is for an effective scientific collaboration based on:
  a common collaborative research approach using underpinning infrastructure
  building trust between scientists with collaborative working practices
  enable the sharing knowledge by delivering capabilities that deliver a high degree knowledge sharing.

## Slide 12: Technical Infrastructure programme launched June 2013
TIRS
Rose development &
migration
TIHP
HPC optimisation
TIFF
File formats – STASH, NetCDF,
and GRIB2
TILS
Land-surface model
interoperability
TIDA
Data assimilation
TIAN
Stabilising and re-engineering
ancillary file system
TICF
Coupling frameworks
OASIS-MCT
TICT
UM configuration testing &
system refresh
TICM
Common shared repositories
& trac environments
TIAV
Data processing &
visualisation
TIAG
Advisory group
Notes: Not going to have time to talk about all of the work packages but will give a flavour of the most important ones and briefly summarise relevant capabilities/milestones and the benefits that can be realised from successful delivery.
A more detailed account of development and capabilities will follow later today.
Each work package is being managed a separate project wherever possible.
There are 11 work packages currently agreed in the theme plan.
Organisation & individuals have been identified to lead work packages.
Proposals for resourcing work packages in 2014/2015 have been submitted by Partners.

## Slide 13: Joint science programme ...
RMED
Regiona model eval / dev
GMED
Global model eval / dev
CMIP6
Joint runs, UKESM eval / dev
TC
Tropical cyclone forecasting
DA
Data Assimilation
Glosea
Joint seasonal forecasting
Notes: Not going to have time to talk about all of the work packages but will give a flavour of the most important ones and briefly summarise relevant capabilities/milestones and the benefits that can be realised from successful delivery.
A more detailed account of development and capabilities will follow later today.
Each work package is being managed a separate project wherever possible.
There are 11 work packages currently agreed in the theme plan.
Organisation & individuals have been identified to lead work packages.
Proposals for resourcing work packages in 2014/2015 have been submitted by Partners.

## Slide 14: ACCESS NWP Systems – APS2 upgrade (2015-16)
Met Office Unified Model
6 hourly 4dVAR
  Global: ~40km (APS1) 25km (APS2)
  Regional: ~12km (APS1)  12km (APS2)
  TC: ~12km (APS1)  12km (APS2)
City Systems
  4.5km (APS1)  1.5km (APS2)
  No Assimilation
  Grey zone -> convection off
  Darwin domain added
Ensembles
  Global None (APS1)  60km (APS2)
  Limited products available initially
Regional
TC
Notes: SREP NWP systems will replace current City systems
Will demonstrate why 0.05deg is an awkward resolution
Relocatable facility available – current jobs run with this (just set to constant lat/lon bounds)
NO ensemble prediction component – need other projects to have completed
Focus on Sydney & Brisbane
Brisbane as great tough training/calibration set
Sydney as best obs network

## Slide 15
APS2 ACCESS-G verifications
March 2015
Comparison between G1 & G2 and UK global forecasts – verification vs analyses
More improvement in Southern Hemisphere than Northern
Australian region
S. Annulus
N. Annulus

## Slide 16
APS2 ACCESS-C Darwin
TC Nathan
IC: 12Z 22 March 2015
1.5km
12 km
6h
24h
18h
12h
6h
24h
18h
12h

## Slide 17: ACCESS NWP future directions
A prime future requirement for operational NWP will be to provide outputs that meet societal needs
Severe weather prediction is a key deliverable
  High resolution: 1-1.5km
  Data assimilation
  Rapid update cycles
  High resolution ensembles
Heavy supercomputing demands - NPP

## Slide 18: ACCESS NWP Plans
 | APS-2 Op: 2016 | APS-3 Op: 2017-2018 | APS-4 Op: 2019-2020
ACCESS-G | 25km {4dV} | 12km {4dVH} | 12km {4dVH/En}
ACCESS-R | 12km {4dV} | 8km {4dVH} | 4.5km {4dVH/En}
ACCESS-TC | 12km {4dV} | 4.5km {4dVH} | 4.5km {4dVH}
ACCESS-GE | 60km (lim) | 30km | 30km
ACCESS-C | 1.5km {FC} | 1.5km {4dVH} | 1.5km {4dVH/En}
ACCESS-CE | - | 2.2km (lim) | 1.5km
ACCESS-X | - | 1.5km {4dVH} | 1.5km {4dVH/En}
ACCESS-XE | - | - | 1.5km

## Slide 19: Towards APS2: ACCESS-G
N512 (25km), L70, UM 8.2 trial system running for over a year now
Complete obs-set, including SSMIS, CrIS/ATMS, with exception of windsat
Just handed-over to ops branch, expected to go operational mid-year.
Aust
Notes: 19
Verification for APS2 ACCESS-G ("G2") trial, against current operational system ("G1"), and UK global operational system, Australian region
Australian Region, Feb 2015

## Slide 20: Towards APS2: ACCESS-G
SH
NH
Notes: 20
Good performance gain over Australia, SH, no improvement over NH. Still unsure why – resolved earlier issues with gravity-wave / topography-resolution interaction, but stumped since.

## Slide 21: Towards APS2: ACCESS-G
Surface verification
  Improvements in first 2-3 days
  2% improvement in wind-speed, 4% in temp
Notes: 21
  Note: Error(G2) – Error(G1) == negative is "good" (G2 better than G1)
  Slight improvement in 10m windspeed, of about 2% mainly during the first two days and in the afternoon and evening
  2m temperature and dewpoint improved by about 4% during the first 3 days biggest gains in first 48 hours and during the afternoon and evening. (i.e. Tmax improved more than Tmin)
  Forecast length shown in boxes ("+30")

## Slide 22: Towards APS2: ACCESS-R
Regional model has same data-streams as global, and UM is upgraded (8.4), but resolution unchanged
  Medium term uncertainty over regional-modelling
Improved local-topography, R-domain-specific covariances
  Verif shows more improvement than we were expecting
Hand-over date June, operational by end of year
Notes: 22
"Uncertainty" – where does regional model fit between increasingly high-resolution global, and the city-based / on-demand very high-resolution systems ??? Can no longer rely on UKMO "NAE" model as a base.
"access-r" (blue) = operational system (R1)
"r2t3" (red) = trial APS2 ACCESS-R (R2) system
Mslp to left, screen-temperature to right. Be careful of the vertical-scales R2-Tscr has worse bias, but difference is small!

## Slide 23: Towards APS2: ACCESS-C
C2 is still a down-scaler (FC-only) system, like C1
Convection-permitting (ala UKV): 1.5km res, down from 4km.
  Significant computational challenge to "fit" on current SC
    Importance of I/O server for R2 (BC and ICs)
    More tightly inter-leave running of "R" and "C", stagger some of the "C" domains in time.
Trial evaluation currently underway
  Several examples of C2 avoiding the coastal-locking of rainfall in certain scenarios in C1.
Hand-over to operations anticipated in July
Notes: 23
"C2" = APS2 ACCESS-C
"UKV" = UKMO 1.5km variable-resolution (stretched-grid)

## Slide 24: Towards APS2: ACCESS-GE
Will be our first ACCESS-based operational ensemble system
  Based on UKMO MOGREPS
  Global ensemble to 10 days
  Global ETKF for initial condition perts
  Stochastic model perturbations
  Currently running 12Z daily at 60 km, 70 levels (N216L70)
Comparable performance to major O/S systems
Hand-over to operations expected in 3rd-quarter
Notes: 24

## Slide 25: APS2: ACCESS-GE
ACCESS-GE
ECMWF
JMA
NCEP
MSLP
December 2014
SHEM TROP NHEM
Notes: 25

## Slide 26: Improved Seasonal Forecast System
Debbie Hudson, Oscar Alves, Harry Hendon

## Slide 27: Background
BoM's seasonal forecasts have become more skilful with recent versions of the system, but user expectations and performance is still inhibiting uptake by users
Increasing demand for multi-week and seasonal forecasts
Present system (POAMA-2) is low resolution (250 km) and based on no longer supported models
Prior to April this year development focussed on POAMA-3 ---150 km resolution with same model configuration as for climate change studies (UM atmosphere, MOM ocean)
POAMA-3 already lower resolution than systems operating at other leading centres and the current approach means that we will always be at least two to four years behind the latest developments available from the UKMO

## Slide 28: Plan
New the system: ACCESS-S
Deliver a high resolution seasonal prediction system at reduced cost, reduced forecast risk and on a significantly shorter time frame compared with the past approach
Use latest version of the UKMO coupled model: UM atmos N216 (~60km in midlats) L85; NEMO ocean 0.25° L75
Implement local data assimilation and ensemble generation
Option for joint hindcasts and forecasts with UKMO
Play significant role in contributing to UKMO development

## Slide 29: Plan: Phase 1
Fast track phase : transfer to operations for trial mid-2016*
UKMO GC3 (stochastic phys, greenhouse gases, etc)
UKMO initial conditions + local ensemble generation
Hindcasts increased from 15 to 25 years
Hindcasts members increased from 3 to 10
Real-time forecasts 2 per day from UKMO + at least 3 per day from BoM
6 months lead (could do longer using local forecasts only)
*Note: exact timelines for delivery depend on funding and supercomputer

## Slide 30: Plan: Phase 2
Full suite phase: transfer to operations for trial mid-2018*
UKMO GC4/5 (reduced tropical biases e.g. Indian Ocean)
Local Coupled EnKF for assimilation and ensemble generation
Hindcasts locally 35+ years (joint with UKMO?)
Hindcasts members at least 10 (joint with UKMO?)
Real-time forecasts at least 5 per day (+UKMO ones?)
1 year lead (?)
*Note: exact timelines for delivery depend on funding and supercomputer

## Slide 31: Rapid Update Cycle – Hourly 1.5km experimental system
Aim: High res. NWP guidance using radar data
Configuration
  3DVAR
    1-hourly analysis cycle,
    data cut-off ~60mins
    Issues with 4dVAR stability
  Latent Heat Nudging
  Test cloud assimilation
  Doppler winds
  Best coverage is over Eastern NSW (Sydney Domain)
  Single polarization → QC via Bayesian classifier
Peter Steinle et al.

## Slide 32: Sydney Forecast Demonstration Project
Late Sep – early Dec 2014
  What new things can we do
  What old things can we do better
Incorporate RUC into forecasting applications
  Forecast Editor/Generator
  Data visualization
  Nowcasting applications
  Post processing applications
Mimic operational forecast office
Some external participants
  For their evaluation
Peter Steinle et al.

## Slide 33
Evaluation of ACCESS-C forecasts of wintertime precipitation over the Snowy Mountains - a comparison with WRF simulations
Vivian Huang, T. Chubb, S. Siems, M. Manton, C. Franklin
12 UTC Sep 27 – 12 UTC Oct 01, 2011: NW and deep moisture
Largest daily precipitation amount of the whole winter of 2011
00UTC Sep 28
00UTC Sep 30

## Slide 34
ACCESS
OBJECTIVE ANALYSIS
WRF_Thompson_default
WRF_Thompson_test
WRF_Morrison_default
WRF_Morrison_test

## Slide 35
Forecast rainfall by ACCESS is highly sensitive to topography.
No significant orographic enhancement
All the simulations capture the onset of the precipitation reasonably well.
WRF significantly underestimates the accumulated amount of rainfall (~50%).

## Slide 36
Satellite overpass: 04:25 UTC July 23, 2013
A-Train track: South Cape
High pressure ridge
SSE(observed)/SSW(models)
Large field of boundary layer (BL) clouds
Aerosols underneath clouds
An Evaluation of ACCESS-C forecasts of Boundary Layer Clouds over the Southern Ocean
Vivian Huang, C. Franklin, S. Siems, M. Manton, T. Chubb, A. Lock

## Slide 37
Evaluation of soundings
ACCESS vs. Hobart
23UTC 22/07/2013
ACCESS vs. aircraft
~04UTC 23/07/2013
Ascent
Descent

## Slide 39: High impact weather modelling team TCs, Bushfires, Aviation, Severe TS, etc.
To improve our understanding of and ability to predict severe weather, including for bush fires, tropical cyclones, severe thunderstorms and heavy rainfall, through the use of high-resolution modelling in conjunction with available observations
Jeff Kepert et al.

## Slide 40: Wind speed and direction Ash Wednesday, 1983
ACCESS simulation on 400-m grid.
Marked wind change
Roll circulations ahead of change from late morning
Strong post-frontal winds caused severe fire behaviour, many deaths
Thunderstorm downdrafts ahead of change
400 m grid
Jeff Kepert et al.

## Slide 41: Plume dynamics LES, 15 m s-1 wind
Jeff Kepert et al.

## Slide 42: Firebrand transport LES, 15 m s-1 wind
8265 particles released every 5 s for 15 min = 1,487,700 total
Only every 100th particle is shown here
478,058 (32.1 %) travel > 1 km
Jeff Kepert et al.

## Slide 43
APS2 ACCESS-TC
Track Verification for 2014-15 Australian Region Storms
5 TCs = Lam, Marcia, Nathan, Olwyn, Pam
  At 0 hrs, Mean TRK Err for 47 Forcs = 23.3 km
  At 24 hrs, Mean TRK Err for 44 Forcs = 76.9 km
  At 48 hrs, Mean TRK Err for 37 Forcs = 136.3 km
  At 72 hrs, Mean TRK Err for 29 Forcs = 235.7 km
Quite impressive in absolute terms.
Positive impact on APS1 ACCESS-TC, out to 48 hours (not shown).
Nice improvements in initialization of vortex and environmental, steering flows.
Some examples of the many good, but still a few poor forecasts.
………………………………………………………………………………………………………………………………..
Noel Davidson, Yi Xiao et al.

## Slide 44: Spray Route Scheme – Revised Parameterisation of Air-Sea Exchanges in High Winds: Impact on Tropical Cyclone Track, Intensity and Rapid Intensification
Time series of simulated central pressure (CP), inner core parameters of maximum wind (VM) and radius of maximum wind (RMW), radius of 34 knots (R34), using the bulk algorithm (CTL) and the spray route scheme (SPY). The best-estimated CP is indicated with ”o”.
Yimin Ma et al.

## Slide 45: NW Australia Extended-Range TC Forecasts
Project initiated by offshore oil and gas, NW Aust
Main aims:
  Forecasts to 5 days
  Better forecasts of genesis and intensity
  Wave forecasts under TCs
Proposed solution:
  Extended domain limited area, not relocatable
  Resolution increase from ACCESS-TC (from 11 km to 4 km)
  4D-Var with vortex specification (bogussing)
  Daily running, not just when a cyclone is named
  One-way coupled to wave model
Some similarities to MetOffice’s P4.4 system, but will include assimilation
Xingbao Wang, Jeff Kepert, Noel Davidson et al.

## Slide 46: Maritime Continent PEG Summary of 12 May 2015 meeting
Modelling: UM AMIP and NEMO-WRF regional coupled models produce less rainfall bias over the MC if increasing the horizontal resolutions, likely due to better simulated orography & diurnal cycle. Mixed layer coupled modelling (KPP) provides a cheap tool and simulates better MJO eastward propagation. Super-parameterized AGCM also provides good MJO propagation.
Model tuning: Modified melting levels reduces rainfall bias over MC. Increasing local SST (0.3C) showed the similar effect.
Process understanding: Cold surge contributes 20-40% rainfall over MC. Bias in horizontal moisture convergence controls the local rainfall bias. Large-scale circulation has minor impacts on coastal rainfall over MC.
Observation: Large uncertainty the MC area including satellite retrievals. Model biases shown will depend on the reference observations. YMC shall provide better quality of observations.
Jing-Jia Luo, Harun Rashid, Hongyan Zhu et al.

## Slide 47: Impact of Buildings and Trees Surface verification over Jun/July 2014
RMSD from Observed |  |  |  |  |  |  | 
 | Screen Temperature (K) |  |  | Screen Dew Point (K) |  | 10m Wind Speed (m/s) | 
MARS ID | 0001 | 3101 | Improv | 0001 | 3101 | 0001 | 3101
Sydney | 1.98 | 1.81 | 9% | 1.87 | 1.73 | 2.08 | 1.96
VicTas | 1.71 | 1.62 | 5% | 1.59 | 1.54 | 2.01 | 1.94
Adelaide | 1.48 | 1.45 | 2% | 1.68 | 1.63 | 1.68 | 1.68
Perth | 1.67 | 1.59 | 5% | 1.86 | 1.78 | 1.88 | 1.94
Brisbane | 2.24 | 1.79 | 20% | 2.18 | 2.04 | 1.59 | 1.55
Darwin | 2.03 | 1.87 | 8% | 2.50 | 2.39 | 1.57 | 1.91
New Urban Parameters and Tree Heights + New Orography-Lakes
Imtiaz Dharssi
OLD
NEW
DIFF

## Slide 48: VERIFICATION of Soil Moisture ANALYSES from Global NWP Models USING Ground Based Observations
Vinod Kumar & Imtiaz Dharssi
Bureau of Meteorology, Melbourne
2015

## Slide 49
CosmOz Soil Moisture Stations
Vinod Kumar & Imtiaz Dharssi

## Slide 50
Soil Moisture Skill Scores: Model vs Observations
Metrics Dec 2013 to Feb 2015 | APS1 (N320) | APS2 (N512) | ECMWF
Mean Correlation | 0.80 | 0.75 | 0.82
Anomaly Correlation* | 0.49 | 0.56 | 0.58
Mean Bias [m3/m3] | -0.06 | -0.01 | -0.08
Mean RMSD [m3/m3] | 0.10 | 0.07 | 0.10
* Anomalies calculated using a 30 day rolling window
Vinod Kumar & Imtiaz Dharssi

## Slide 51: Solution to Eliminate Spurious Wind-Gusts from APS1(2) ACCESS-C over VicTas Domain
Yimin Ma et al.
Top left:
  Wind gust spikes
Bottom Left:
  Sampled locations
Top and bottom right:
  Time series of wind gusts at two locations; original and new formulae

## Slide 52: Fixing a problem in direct solar radiation
A problem in direct solar radiation in ES radiation has been found
It is due to the application of delta-Eddington scaling approximation to the direct solar radiation; it should only apply to the diffuse radiation
Effects: direct solar radiation is overestimated and diffuse radiation is underestimated. Both affect land surface processes
Fix has been applied to ACCESS UM8.2, 8.4 versions and vn10.1 shared repository
Zhian Sun et al.

## Slide 53
Total flux
Direct before fix
Direct after fix
SES2
ES
Zhian Sun et al.

## Slide 54
AMIP & T-AMIP
Precip mean and bias relative to GPCP
ACCESS1.3 N96L38
GA6N96L85
AMIP
AMIP
T-AMIP
T-AMIP
Greg Roff

## Slide 55: ACCESS-CABLE for NWP: preliminary results from Transpose AMIP experiments
Huqiang (Hugh) Zhang, Greg Roff
Bureau of Meteorology
h.zhang@bom.gov.au
Acknowledgement:
CABLE team (in particular: Jhan Srbinovsky, Lauren Stevens technical assistance)
ACCESS/ESM team
CAWCR: Collaboration for Australian Weather and Climate Research

## Slide 56
GA6+CABLE
GA6+ JULES
Pr obs
CASE 2009-01-16
Fcst day1 day2 day3 day4 day5
Huqiang Zhang & Greg Roff

## Slide 57: High Ice Water Content Modelling Study
Charmaine Franklin, Alain Protat
19 May 2015
Oceans and atmosphere
Acknowledgements: Use of MONSooN under the ASCI project

## Slide 58: Motivation Scientific motivations
Observations of clouds with high ice water content but low radar reflectivity challenges our understanding of cloud processes
Determine the small ice particle formation mechanism: nucleation or ice multiplication
Determine the evolution of the mixed-phase in deep convective clouds - how does the liquid/ice water fraction change
Improve the simulation of deep convective cloud systems
Charmaine Franklin & Alain Protat

## Slide 59: High Ice Water Content Modelling Study
Evaluate ACCESS 1km (8.5 PS32) simulations of tropical convection
Investigate the controls on phase composition in the model
Examine the effects of dynamics, turbulence and microphysical parameterisations
Darwin mesoscale convective system case study February 18 2014
Evaluation using CPOL radar, radiosonde, satellite and aircraft obs
= control, PS32 using new dynamics
= ENDGame even newer dynamics
= ENDGAME using nd boundary conditions
= 3d Smagorinsky rather than blended vertical diffusion
= no generic ice size distribution parameterisation
= nopsd but with additional ice prognostic
= qcf2 but with Hallett-Mossop ice splintering parameterisation
= qcf2 but with cloud droplet number of 500 not 100
= qcf2 but without snow-rain collisions producing graupel
= qcf2 but without graupel
= qcf2 but with freezing rain a source of graupel
= qcf2 but with Marshall-Palmer rain drop size distribution
Charmaine Franklin & Alain Protat
Notes: All simulations but eg use the bcs from a 4 km nd simulation. The eg simulation is nested in its own 4 km run. Given the differences seen I wanted to look at the effect of the different bcs and have another eg simulation using the nd bcs.
The green and black lines are microphysics changes that I won’t go through but will mention a few as we go through the figures.

## Slide 60: Sensitivity of the ACCESS forecast model statistical rainfall properties to resolution
Hanh Nguyen
Alain Protat
Michael Whimpey

## Slide 61
Hanh Nguyen & Alain Protat
Effect of horizontal resolution on model errors over Darwin
OBS
MOD
12km
4km
Daily mean rainfall:
Land/sea contrast error in the model of opposite sign with change from 12km to 4km
PDF:
Only the 4km version shows realistic PDF with reduced light rain BUT overestimate heavy rain (>50mm/hr)
Diurnal cycle:
Only the 4km version reproduces the correct timing of the total domain rainfall peak at 15LT as opposed to too early 12LT
Daily mean rainfall
Hourly rainfall PDF
Solid: CPOL
Dash: ACCESS
Diurnal cycle
Total domain rain
Rain intensity
Rain frequency

## Slide 62: Future challenges
Weather prediction with coupled atmosphere/land surface/ocean models
  Coupled data assimilation
Ensembles
  How to fully capitalise on potential
Environmental prediction
  Chemistry: coupled or offline; assimilation
Data
  Explosive increase in and variety of data from sounders
  How to handle and assimilate the data
Verification of high resolution models, severe weather events
Running models on next generation of supercomputers
  ~ 1 million cores
Kamal Puri

## Slide 63
Michael Naughton
+61 3 9669 44311
M.Naughton@bom.gov.au
Thank you…

## Slide 64: Met Office science
And science partnerships
3 February 2016

## Slide 65: Advice across all timescales
Forecast lead-time
Confidence boundary
Now
Hours
Days
1-week
1-month
Seasonal
Decadal
Climate
Past climate
Analysis of past weather observations to manage climate risks
Eg. Agriculture: informs crop choice, planting to yield optimisation and minimise crop failure risk.
Predicting routine and hazardous weather conditions.
Public, emergency response, international Disaster Risk Reduction
Monthly to decadal predictions - probability of drought, cold, hurricanes….
Contingency planners, national and international humanitarian response, government and private infrastructure investment
Global and regional climate predictions.
Informs mitigation policy and adaptation choices. Impacts on water resources, heat stress, crops, infrastructure.
Notes: The Vuvuzela of seamless prediction:
The Met Office is able to make predictions on all timescales from now until a century ahead.
Analysis of past weather data is also useful to understand weather risks today – for example what is the likelihood of a particular storm event occurring.
On longer timescales the confidence boundary gets wider – however if the climate information is applied in an appropriate manner it provides extremely useful information to inform adaptation decision making.

## Slide 66
N x Global coupled model at ~10km with lead times of days to years:
Synoptic drivers
N x local coupled model at ~<=1km :
Local meteorology
PDF of local hazard:
Impacts
Met Office Modelling Strategy

## Slide 67
© Crown copyright Met Office
UK Operational Forecasting Models: Based on the Unified Model developed in partnership
Monthly to Seasonal
60 km atmosphere
¼ deg. ocean
2 ensemble members per day
Regional 4km
Global 17km
UK 1.5km
T+5 days twice/day
T+60 hour twice/day
+Regional ensemble
T+5 days twice/day
T+2 days twice/day
+Global ensemble
36 hour lead time
8 times/day
+UK ensemble 2.2 km
70 levels
85 with stratosphere
Regional models can be re-located rapidly to anywhere on the globe for weather or climate…
Notes: 67

## Slide 69
Science partnerships
There are about 600 staff in the science area of the Met Office
Science partnerships aims to maximise the value of science and modelling collaboration to the Met Office and its partners
Most of the team – including myself are also active in science research and/or modelling

## Slide 70
Hours Days Weeks Months Seasons Decades Centuries
Deterministic
Ensembles
GloSea
Decadal
Climate Change
NWP - Atmosphere, Ocean, Waves
Ensembles
Multi-model ensembles
Earth system models
OBGC; land ice; chemistry
Physical models
Atmosphere; ocean; ice; land
Unified modelling partnership
Met Office Academic partnership
JWCRP
Notes: 70
e.g. UK ESM strategy
e.g. Next-generation dynamical cores
First jointly funded programme of its kind, initially funding 5 joint post-docs
More recently developed joint calls/workshops in Upper Ocean mixing
e.g. MONSooN
- ‘Operational’ since December 2009
Currently supporting 15 projects involving more than 150 scientists
Utilisation running at 93%
e.g. FAAM
- Development and maintenance of major investments in joint research facilities

## Slide 71
International UM partnerships
Jointly developing a world leading seamless modelling system in a coordinated way
Shared science, model evaluation and technical development:
  Joint process evaluation groups
  Technical infrastructure teams
  User workshops & tutorials
Operational users complemented by:
  research partners in national / international universities & organisations
  capacity building consultancy projects with other partners
A foundation for relationships with other organisations:
  Science & model development
  Weather & climate services
  Jointly growing our businesses

## Slide 72
Principles of UM partnerships
The more a UM partner can invest and support itself, the more a partner can influence strategic direction of model development and own the UM
Core partners:
Commit 4FTE to joint development
Locally run and support operations & upgrades and fund central support
Member of board sets direction of joint work, controls funds & influences decisions on model development
Research partners:
Non operational users able to commit to joint development
May fund central support if needed
Associate partners:
Some commitment to joint development
Locally run and support operations & upgrades and fund central support
Feed views to the board
Board
Governing and decision body
Representative from each core partner institute
Technical advisory group
Advises board, plans and coordinates technical work
Representative from all relevant partner institutes
Science advisory group
Advises board, plans and coordinates science work
Representative from all relevant partner institutes
Ad-hoc projects
May be a need to have specific projects from time to time
Representative from all relevant partner institutes

## Slide 73
© Crown copyright Met Office
Global NWP Index (v analysis) basket % difference relative to Met Office
Maintaining our global standing

## Slide 74: Technical Infrastructure Programme Motivation
Initiated in June 2013 to resolve the priority weaknesses of the research and operational infrastructure.
Goal is a more streamlined, flexible system that is easier to use and adopt for scientific research and operational environments.
Key activities are reviewed annually in a Technical Infrastructure Programme Plan.
Program vision is for an effective scientific collaboration based on:
  a common collaborative research approach using underpinning infrastructure
  building trust between scientists with collaborative working practices
  enable the sharing knowledge by delivering capabilities that deliver a high degree knowledge sharing.

## Slide 75: Technical Infrastructure programme launched June 2013
TIRS
Rose development &
migration
TIHP
HPC optimisation
TIFF
File formats – STASH, NetCDF,
and GRIB2
TILS
Land-surface model
interoperability
TIDA
Data assimilation
TIAN
Stabilising and re-engineering
ancillary file system
TICF
Coupling frameworks
OASIS-MCT
TICT
UM configuration testing &
system refresh
TICM
Common shared repositories
& trac environments
TIAV
Data processing &
visualisation
TIAG
Advisory group
Notes: Not going to have time to talk about all of the work packages but will give a flavour of the most important ones and briefly summarise relevant capabilities/milestones and the benefits that can be realised from successful delivery.
A more detailed account of development and capabilities will follow later today.
Each work package is being managed a separate project wherever possible.
There are 11 work packages currently agreed in the theme plan.
Organisation & individuals have been identified to lead work packages.
Proposals for resourcing work packages in 2014/2015 have been submitted by Partners.

## Slide 76: Joint science programme ...
RMED
Regiona model eval / dev
GMED
Global model eval / dev
CMIP6
Joint runs, UKESM eval / dev
TC
Tropical cyclone forecasting
DA
Data Assimilation
Glosea
Joint seasonal forecasting
Notes: Not going to have time to talk about all of the work packages but will give a flavour of the most important ones and briefly summarise relevant capabilities/milestones and the benefits that can be realised from successful delivery.
A more detailed account of development and capabilities will follow later today.
Each work package is being managed a separate project wherever possible.
There are 11 work packages currently agreed in the theme plan.
Organisation & individuals have been identified to lead work packages.
Proposals for resourcing work packages in 2014/2015 have been submitted by Partners.

## Slide 77
Facilitating UM partnerships
Primary support for operational NWP users of the UM - BoM, KMA, NIWA, NCMRWF, SAWS, AFW, ICM, MSS including regional cutouts, frames ...
Covers science/technical/practical areas - all aspects of UM systems and Met Office science, e.g. building/running, configurations, ancillaries, data provision, modelling strategy/plans, data transfers, software installation, wikis, newsgroups, shared repository service, hosting visiting scientists ...
Training in UM installation, Rose/cylc, tutorials ...
Development of joint science / technical programmes prioritised by stakeholders, e.g. Rose, file formats, ancillaries, tropical convection, NWP problems
© Crown copyright Met Office

## Slide 78: Joint Weather and Climate Research Programme (JWCRP)
Shared science
UKESM – Next-generation Earth System Model
Gung-ho – Next-generation dynamical cores
UPSCALE – High resolution climate modelling
Shared research facilities
MONSooN – High performance . computing
FAAM – Research aircraft
JWCRP facilitates joint research between NERC and the Met Office – to ensure that the UK strengthens its leading international position in weather and climate science
Notes: 78
e.g. UK ESM strategy
e.g. Next-generation dynamical cores
First jointly funded programme of its kind, initially funding 5 joint post-docs
More recently developed joint calls/workshops in Upper Ocean mixing
e.g. MONSooN
- ‘Operational’ since December 2009
Currently supporting 15 projects involving more than 150 scientists
Utilisation running at 93%
e.g. FAAM
- Development and maintenance of major investments in joint research facilities

## Slide 79
MOAP: Met Office Academic Partnership
Building on existing strengths
MOAP provides the Met Office access to a cluster of 1000+ scientists working in diverse areas of relevance to its science strategy.
MOAP delivers over £3m per annum of key science to the programme through joint projects.
Jointly funded professorships in the Universities and well managed coordinating committees form the foundation of MOAP activities.
In any year, typically MOAP will support:
  Various visiting scientists to the Met Office
  Around 30 jointly supervised PhD studentships
  Around 15 of our staff as honorary professors
  Award a range of undergraduate prizes
  Have several Met Office staff members undertaking external PhDs

## Slide 80: Thank You

## Slide 81: GA/GC development process RA development process? CS workshop Feb 2016
Model
Development
Model
Assessment
Process
Evaluation
Groups
Top 10
problems
Annual
cycle
Progress
Reviewed annually