## Slide 1: Verification of ACCESS surface winds for wave modelling
Stefan Zieger
11 June 2021

## Slide 2: Outline
Observations
Verification
  Hindcast
  Forecast
Summary

## Slide 3: Observations
Daily global coverage
Scatterometer winds (ASCAT)
  Active system based on C-band radar
  Wind speed range: 0 – 25 m/s
  Error: 0.98 m s-1
Radiometer winds (AMSR2)
  Passive microwave system based on brightness temperature.
  Wind speed range: 0 – 30 m/s
  Error: 0.9 m s-1 (no-rain conditions)
Source: Remote Sensing Systems

## Slide 4: ACCESS-G3 verification – surface winds
Period: June – October 2020
Recurring ACCESS-G3 surface fields (0-11 hours; hourly)
Resolution: ~12km
Radiometer winds (AMSR2)
Scatterometer winds (ASCAT)
RMSE: 1.21 to 1.26 m s-1
R: 0.946 to 0.950
SI: 0.15 to 0.16
BIAS: -0.23 to -0.11 m s-1

## Slide 5: ACCESS-G3 surface wind verification
Period: 01/06/2020 – 01/10/2020
Radiometer wind speed error: 0.9 m s-1 (no-rain conditions)
Scatterometer wind speed error: 0.98 m s-1
Young & Donelan (2018) identified systematic differences in radiometer winds speed that vary in latitude and season.
Radiometers
Scatterometers

## Slide 6: Wave model
 | ST | OM3 | SNL | WINDS | COST | NAMELIST PARAMETERS
OPR | ST4 | No | NL1 | 1.45 | 0.22 | —
S01 | ST6 | No | NL1 | 1.00 | 0.91 | Default LAMBDA=0.250 NLPOP=3.00E7 SINA0=0.09
S02 | ST6 | Yes | NL1 | 1.00 | 1.02 | RWNDC=0.5
S03 | ST6 | Yes | NL3 | 1.00 | 1.60 | NQDEF=5 RWNDC=0.5
S04 | ST6 | No | NL3 | 1.00 | 1.54 | NQDEF=5
S05 | ST6 | No | NL1 | 1.02 | 0.91 | —
S06 | ST6 | Yes | NL1 | 1.02 | 0.93 | RWNDC=0.5
S07 | ST6 | Yes | NL3 | 1.02 | 1.66 | NQDEF=5 RWNDC=0.5
S08 | ST6 | No | NL1 | 1.01 | 1.04 | —
S09 | ST6 | Yes | NL1 | 1.01 | 0.91 | RWNDC=0.5
S10 | ST6 | Yes | NL1 | 1.02 | 1.02 | RWNDC=0.55
S11 | ST6 | Yes | NL1 | 1.05 | 1.07 | LAMBDA=0.237 NLPOP=2.13E7 RWNDC=0.5
S12 | ST6 | Yes | NL1 | 1.05 | 1.07 | LAMBDA=0.233 NLPOP=1.20E7 DIA OPT w/ NLOPT RWNDC=0.5
S13 | ST6 | Yes | NL3 | 1.05 | 1.20 | NQDEF=1 QPARMS = 0.234,0.0,-1.0,2.13E7,2.737E5 RWNDC=0.5
S14 | ST6 | Yes | NL1 | 1.05 | 1.06 | LAMBDA=0.237 NLPOP=2.13E7 RWNDC=0.55
S15 | ST6 | Yes | NL1 | 1.03 | 1.06 | LAMBDA=0.237 NLPOP=2.13E7 SINA0=0.08 RWNDC=0.60
S16 | ST6 | No | NL1 | 1.05 | 0.93 | LAMBDA=0.237 NLPOP=2.13E7 SINA0=0.08
S17 | ST6 | No | NL1 | 1.02 | 0.93 | LAMBDA=0.237 NLPOP=2.13E7 SINA0=0.08
S18 | ST6 | No | NL1 | 1.03 | 0.93 | LAMBDA=0.237 NLPOP=2.13E7 SINA0=0.08
S21 | ST4 | No | NL1 | 1.43 | 1.00 | —
S22 | ST4 | Yes | NL1 | 1.45 | 1.07 | RWNDC=0.5
S23 | ST4 | No | NL1 | 1.45 | 0.98 | —
S24 | ST4 | No | NL1 | 1.40 | 0.95 | —
S25 | ST4 | Yes | NL1 | 1.42 | 1.08 | RWNDC=0.5
Cost 1.00 translates to 12 minutes runtime per day simulation (384 CPUs).

## Slide 7: Hindcast verification – altimeter
OPR
S15

## Slide 8: Hindcast verification – altimeter
OPR
S15

## Slide 9: Forecast verification
RMSE in surface wind speed increases linearly with lead time.
Correlation decreases with lead time.
Performance around Australia is generally better than global.

## Slide 10: Forecast verification
Wind speed
Wave height

## Slide 11: Summary
RMSE, MAE and SI increase with lead time
No change in bias and standard deviation with lead time
No drift in ACCESS-G3 surface winds (persistent boundary conditions)
Error due to phasing ?
REG. | LEAD TIME | E | AE | B | R | I | SI | FIT0 | STD(M) | STD(O)
GLOBAL | +12 | 1.28 | 0.90 | -0.27 | 0.942 | 0.942 | 0.15 | 0.96 | 3.69 | 3.68
 | +24 | 1.43 | 1.02 | -0.25 | 0.927 | 0.943 | 0.17 | 0.96 | 3.69 | —
 | +36 | 1.58 | 1.12 | -0.24 | 0.910 | 0.944 | 0.19 | 0.96 | 3.69 | —
 | +48 | 1.74 | 1.24 | -0.23 | 0.891 | 0.946 | 0.21 | 0.96 | 3.69 | —
 | +60 | 1.91 | 1.35 | -0.23 | 0.868 | 0.946 | 0.23 | 0.96 | 3.69 | —
 | +72 | 2.08 | 1.48 | -0.23 | 0.842 | 0.947 | 0.25 | 0.95 | 3.69 | —
 | +84 | 2.27 | 1.61 | -0.22 | 0.812 | 0.948 | 0.27 | 0.95 | 3.68 | —
 | +96 | 2.46 | 1.75 | -0.21 | 0.778 | 0.950 | 0.30 | 0.94 | 3.68 | —
 | +108 | 2.66 | 1.89 | -0.21 | 0.740 | 0.951 | 0.32 | 0.94 | 3.68 | —
 | +120 | 2.85 | 2.03 | -0.21 | 0.700 | 0.952 | 0.35 | 0.93 | 3.67 | —
 | +132 | 3.03 | 2.17 | -0.24 | 0.660 | 0.951 | 0.37 | 0.92 | 3.67 | —
 | +144 | 3.22 | 2.31 | -0.24 | 0.616 | 0.949 | 0.39 | 0.91 | 3.67 | —
 | +156 | 3.37 | 2.43 | -0.26 | 0.578 | 0.948 | 0.41 | 0.90 | 3.67 | —
 | +168 | 3.51 | 2.54 | -0.27 | 0.543 | 0.946 | 0.43 | 0.90 | 3.68 | —

## Slide 12: Questions?
Stefan Zieger
+61 3 9669 4813
stefan.zieger@bom.gov.au