## Slide 1: ACCESS 1.0/1.3 Coupled Model in Rose
Ian Campbell, Peter Uhe
Martin Dix
26th March 2014
www.cawcr.gov.au

## Slide 2
Coupler
OASIS 3.2.5
Atmosphere
HadGEM2 r1.1 or
HadGEM3 GA 1.0
Sea Ice
CICE 4.1
Land Surface
MOSES or CABLE 1.8
Ocean
GFDL MOM4p1
ACCESS 1.0 and 1.3
Notes: Explain Met Office climate model development

## Slide 3: The ACCESS Model CMIP5 configurations
ACCESS 1.0
  Atmosphere: HadGEM2-A r1.1 configuration
      MOSES land surface scheme
ACCESS1.3
  Atmosphere: HadGEM3-A r1.1 configuration (GA 1.0)
    CABLE 1.8 land surface
      Almost no dust
    PC2 cloud scheme
      Bugfixes and tuning
  Atmosphere resolution N96 1.875x1.25 degrees, 38L
    Full GHG, aerosol, volcanic, solar forcings
    Fixed vegetation
Notes: Can also run atmosphere alone (AMIP) or AusCOM (ocean + sea-ice). UM vn7.3
Early testing also considered HadGEM2 + CABLE (1.1), and HadGEM3 + MOSES (1.2)
  Local changes to atmosphere in HadGEM3. Except for change from RH based CAPE closure to vertical velocity based CAPE closure this is GA1.0. Thanks to Charline for providing the files to help sort this out.
Triple cloud scheme

## Slide 4: Global surface air temperature Anomalies relative to 1880-1920 average
The Centre for Australian Weather and Climate Research A partnership between CSIRO and the Bureau of Meteorology

## Slide 5: ACCESS 1.4
Based on ACCESS 1.3
Includes some bug fixes
CABLE 2.0 with carbon cycle
Oasis MCT

## Slide 6: ACCESS 2.0
Hoping to release an interim version towards end of year
Atmosphere - UM GA6.0 configuration (N96 L85)
Ocean – MOM6
Ice – CICE 5
Coupler: OASIS MCT

## Slide 7: Weaknesses of current coupled model setup
Existing environment is a hurdle, particularly for new users
  Coupled model much harder to use than atmospheric model
Coupled model scripts are a mixed combination of configuration and job control
  Difficult to share jobs
  Only ad hoc revision control
  Can be difficult to continue runs after problems
We’ve seen many advantages with the job database and UI for the atmospheric model and would like to bring these to the coupled model

## Slide 8: Advantages of Using Rose suites
Single Interface for editing various models MOM4, CICE and UM
Simple mechanism for sharing or copying suites between users
Automate additional steps (Eg post processing data into CMIP5 format)
Improve traceability of suite development

## Slide 9: Example Suite au-aa025
Historical Run
Runs from 1951 until 2001
Incorporates Scripts from ACCESS 1.0 Coupled Model
Includes build steps for MOM4, UM 7.3 and CICE models

## Slide 10: Checking out/Editing the Model
On accessdev
  $ rosie checkout au-aa025
  $ rose edit -C ~/roses/au-aa025
Allows users to edit
  Top Level Variables
  Environment variables
  Namelists
  Input data files
  Configuration of the Post Processing of data

## Slide 11: Top Level Items

## Slide 12: Editing the Model

## Slide 13: Running the Model
To run the Model on Accessdev
  $ rose suite-run –C ~/roses/au-aa025
Alternatively click on the play icon in the Rose edit interface
What it does?
  Builds the various models
  Runs the model from 1951 in 3 month chunks
  Installs and runs the suite in $HOME/cylc-run
  Work and Share directories under /short/$PROJECT/$USER/cylc-run

## Slide 14: Cylc Window

## Slide 15: Viewing the Output
Data files on Raijin
  /short/$PROJECT/$USER/cylc-run/au-aa025/share/data/history
Data post processed into CMIP5 format
  /g/data1/$PROJECT/$USER/CMIP5/output/CSIRO-BOM/ACCESS1-0/au-aa025
Notes: This is monthly mean surface air temperature for Jan 1960
import iris
import iris.quickplot as qplt
import matplotlib.pyplot as plt
import numpy as np
cubes = iris.load('au-aa025.pa-1960001001', 'air_temperature')
qplt.contourf(cubes[0],np.arange(210,315,5))
plt.gca().coastlines(resolution='50m')
# plt.show()
plt.savefig("/short/p66/mrd599/junk.png")

## Slide 16: When things go wrong!!
Rose log files
  Suite log files on Accessdev
    $HOME/cylc-run/au-aa054/log/suite/log
    $HOME/cylc-run/au-aa054/log/suite/out
    $HOME/cylc-run/au-aa054/log/suite/err
  Job log files on Raijin
    $HOME/cylc-run/au-aa054/log/job/TASK.YYYYMMDD.N.err
    $HOME/cylc-run/au-aa054/log/job/TASK.YYYMMDD.N.out
  Log files can be also viewed via the web interface Rose Bush
    https://accessdev.nci.org.au/rose-bush/

## Slide 17: Future Development
Final release next month
  Completed interface with the UMUI
  Completion of MOM meta data
Further down the track
  ACCESS 2.0
  Completion of interface with UM with release of UM 9.1

## Slide 18: Further Information
Wiki
  https://trac.nci.org.au/trac/access/wiki/ACCESS1.0_rose
  https://trac.nci.org.au/trac/access/wiki/RunningRoseAcessdev
Rose
  http://metomi.github.io/rose/doc/rose.html
Cylc
  http://cylc.github.io/cylc/

## Slide 19: Thank you
The Centre for Australian Weather and Climate Research
A partnership between CSIRO and the Bureau of Meteorology
Ian Campbell
Phone: 03 9616 8412
Email: i.campbell@csiro.au
Web: www.cawcr.gov.au
Thank you
www.cawcr.gov.au